## Slide 1: The r’s Complement
N, a positive number.
r is the base of N with an integer part of n digits.
The r’s complement of N is defined as rn-N for N≠0.
Find 10’s complement of (25.639)10
    Here N=25.639, r=10, n=2
    So Answer will be 102-25.639=74.361
Find 2’s complement of (1011.101)2
    Here N=1011.101,r=2,n=4
    So answer will be (24)2-1011.101=10000-1011.101=0100.011

## Slide 2: Substraction with r’s Complements Example
                Subtract (76425 – 28321) using 10’s complements.
Substract (28531 – 345920)

## Slide 3: Substraction with r’s Complements Example
Subtract (11010011 – 10001100) using 2’s complement.
2’s complement of 10001100 is 01110100
                1 1 0 1 0 0 1 1
                + 0 1 1 1 0 1 0 0
                Carry 1 0 1 0 0 0 1 1 1
The difference is positive and is equal to 01000111
Q: Subtract (1000100 –1010100) using 2’s complement.
2’s complement of 1010100 is 0101100
1000100
+ 0101100
no carry 1110000
Answer will be 2’s complement of 1110000= – 0001000

## Slide 4: The (r-1)’s Complement
N, a positive number.
r is the base of N with an integer part of n digits and fraction part of m digits.
The (r-1)’s complement of N is defined as rn-r-m-N for N≠0.
Find 9’s complement of (25.639)10
    Here N=25.639, r=10, n=2 and m=3
    So Answer will be 102-10-3-25.639=99.999-25.639=74.361
Find 1’s complement of (1011.101)2
    Here N=1011.101, r=2, n=4 and m=-3
    So answer will be (24)2-(2-3)2-1011.101=1111.111-1011.101=0100.010

## Slide 5: Substraction with (r-1)’s Complements example
  Example: Suntraction (28321 – 76425) using 9’s complements
  Answer 9’s complement of 76425 is 23574
  Then add 28321
  +23574
  51895
  Answer will be 9’s complement of 51895 is – 48104

## Slide 6: Substraction with (r-1)’s Complements example
Example: Perform subtraction operation Y-X=1000011-1010100